Coordination of Autonomous Aerial Vehicles
ACCESS Summer Project
June - August 2015

---
Aim
- Design a computer program to fly a quadcopter
- Make a software architecture that easily can be extended

---
IRIS+
- Has internal software that transforms roll, pitch, throttle and yaw to motor speeds
- Can fly for 15 min
- Able to carry about 500 g

---
Overview
Mocap
Security Guard
Blender
Controller

---
Security features
Will land if
- Motion caption signal is lost
- Out of safety zone
- Landing requested

---
Simulator
- Same interface as real quadcopter
- Test code in simulation before real world

---
GUI
Different plugins for different things – more flexible
The GUI should be able to
- Take inputs from user
- Show outputs to the quadcopter
- Show status of quadcopter

---
Some pictures of GUI

---
Trajectory following
Generate points for the quad with
- Position
- Velocity
- Acceleration

---
PID
- Quadcopter largely affected by battery voltage, making integral part important
- Performace?
- Error around a couple of centimeters are required for finer tasks

---
Cool RViz picture?

---
Obstacle avoidance
- Potential between quadcopter and obstacle
- Pushes the quadcopter away from the obstacle, to a lower potential
- Simple type: Ignoring z-direction, giving a 2D problem
Demo/film

---
Leader following
- First quadcopter: Follow trajectory
- Second quadcopter: Keep constant offset to first quadcopter
Demo/film

---
Load lifting
A quadcopter with a gripper can transport a load by
- Read and go to position of load
- Grip load
- Lift and transport load through a given trajectory
- Release load
Demo/film

---
Load lifting controller?
Demo/film?

---
Thanks for your attention!
- Questions?
- Look forward to the demonstation!